# SAMPLE RESPIRATORY PROTECTION PROGRAM

I.     Introduction

In  the control  of  those  occupational  diseases caused  by  breathing air

contaminated  with  dusts,  fogs,  fumes,  mists,  gases,  smokes,   sprays

or    vapors,   the   primary   objective  shall  be  to  prevent  atmospheric

contamination. This shall be accomplished as far as feasible by accepted

engineering  control measures  (for  example,  enclosure  or confinement

of  the  operation,  general  and local  ventilation, and substitution of less

toxic materials). When effective engineering controls are not feasible, or

while  they  are  being   instituted,  appropriate  respirators shall be used.

II.      Purpose and scope

The  practices  and  procedures  described here constitute the respiratory

protection  program  under  which respirators are effectively  utilized  at

(name of company) _________________________________________.

III.      Responsibility

A.   ________________________________ (title or name of one person)

is the  respirator  program  administrator.   He/she  is responsible  for:

- Administering the overall program.

- Implementing training and instruction programs.

- Ensuring that medical evaluation procedures are implemented.

- Selection and provision of appropriate respirators.

# B.   Supervisors are responsible for ensuring that the respiratory  protection

procedure is implemented in their particular areas.Duties of supervisors

include:

- Ensuring  that  employees  under  their  supervision  have  received

appropriate  training,  fit testing,  and  annual  medical  evaluations.

- Ensuring the availability of appropriate respirators and accessories.

- Being  aware  of  tasks  requiring  the  use of respiratory protection.

- Enforcing the proper use of  respiratory protection when necessary.

- Ensuring  that  respirators  are   properly  cleaned, maintained  and

stored according to the respiratory protection plan.

- Ensuring that respirators fit well and do not cause discomfort.

- Monitoring work areas and operations to identify respiratory hazards.

# C.  Each employee has the responsibility  to wear his or her  respirator  when

and where required and in the manner in  which  they  were  trained  and:

- Care for and maintain their respirators as  instructed, and store  them

in a clean sanitary location.

- Inform the supervisor if the respirator no longer fits well, and request

a new one.

- Inform  the  supervisor or  program administrator  of any  respiratory

hazards that they feel are not adequately addressed in the work place

and  of  any  other  concerns  that  they have  regarding the  program.

- Respirator Selection

___________________ (program administrator) will select respirators to be

used  on  site,  based  on  the hazards to which workers are exposed. He will

conduct a  hazard evaluation for each operation,  process,  or work area that

will include:

- Identification and development of a list of hazardous substances used in

the workplace, by department, or work process.

- Review  of work processes to determine  where  potential  exposures to

these hazardous substances may occur.

- Exposure  monitoring  to  quantify potential  hazardous exposures.

End of Service Life Indicators will be used. If there is no ESLI appropriate for conditions in the employer's workplace, the employer implements a change schedule for canisters and cartridges that is based on objective information or data that will ensure that canisters and cartridges are changed before the end of their service life. The employer shall describe in the respirator program the information and data relied upon and the basis for the canister and cartridge change schedule and the basis for reliance on the data.

# EXPOSURE

DEPARTMENT   CONTAMINANTS       LEVEL       PEL   CONTROLS

(8-hr  TWA)

_____________   ________________   __________   ____    ___________

_____________   ________________   __________   ____   ___________

_____________   ________________   __________   ____   ___________

_____________   ________________   __________   ____   ___________

_____________   ________________   __________   ____   ___________

_____________   ________________   __________   ____   ___________

- Medical Evaluations

  - __________________ (program administrator) is responsible for  seeing

that medical evaluations are conducted to determine that employees who

are required to, or those who are allowed to voluntarily  wear respirators

are medically able to do so.

  - ____________________ ( name of licensed health care professional)  of

_________________________ (name of clinic or hospital)   will provide

the medical evaluations.

  - Medical evaluations will be conducted using Appendix C of the standard.

__________ (program administrator)  will give  a  copy to all employees

requiring medical evaluations to complete and  ____________________

___________________ (how to send or take to doctor or clinic/hospital).

  - Follow-up  medical  exams  will  be  granted  as  found necessary  by the

_____________________________________ (doctor or clinic/hospital).

  - All employees will be granted an opportunity to speak with  __________

(doctor/licensed health care professional) about their medical evaluation,

if they request to do so.

  - ____________(program administrator) will provide _________________

(name of doctor or clinic/hospital) with a copy of this program, a copy of

the OSHA respirator standard, a list of hazardous substances in the  work

place,  the  employee’s  job  title,  proposed  respirator  type  and  weight, length  of  time  required to wear respirator, expected physical work load,

potential  temperature  and  humidity  extremes  and  protective  clothing required.

  - After an employee has received clearance and begun to wear a respirator,

additional medical evaluations will be provided when:

    - the employee reports signs/symptoms  related to their ability  to use  a  respirator,  such  as  shortness of breath, dizziness, chest

pains, or wheezing.

    - ___________________ (doctor or clinic/hospital) or supervisor

informs  the  program  administrator that the employee needs to

be re- evaluated.

    - information from  this  program,  including observations  made

during  fit  tests and   program  evaluation indicates a  need  for

re-evaluation.

    - a  change  occurs in workplace  conditions  that may impose an

additional physiological burden on the employee.

# PERSONNEL INCLUDED IN MEDICAL SURVEILLANCE PROGRAM

WORK PROCEDURE/         TYPE

NAME        DEPARTMENT        JOB DESCRIPTION   RESPIRATOR

__________       ______________    ___________________  ____________

__________       ______________    ___________________  ____________

__________       ______________    ___________________  ____________

__________       ______________    ___________________  ____________

__________       ______________    ___________________  ____________

- Fit Tests

  - ____________ (program administrator) is responsible for conducting fit

tests for all employees required to wear  tight-fitting  respirators.

  - Fit tests must be conducted:

    - before  employees  are   allowed   to   wear    any   tight-fitting facepiece respirator.

    - when there are changes  in  the  employee’s physical  condition

that could affect  respiratory fit.

    - at least annually thereafter.

    - using the make, model, and size of respirator they will actually

use.

e.   using  OSHA approved fit test protocols found in  Appendix B

of the OSHA standard.  The methods in use  at this facility are

______________ (qualitative) and ___________ (quantitative).

.

VII.         Respirator Use

- Employees must use their respirators in accordance with the training they

receive.

- Employees  shall  conduct  user  seal  checks  each  time  they  wear their

respirator,  using  either the positive or negative pressure check specified

in  appendix B-1 of the respiratory protection standard.

- Employees  must  be  permitted  to  leave  the  work area  to  clean  their

respirator, change filters or cartridges, replace parts, or  to  inspect  their

respirator if necessary.

- Employees must not be permitted to wear tight-fitting respirators if they

have any condition such as facial scars, facial hair,  or missing dentures,  that prevents them from achieving a good seal.

# PERSONNEL INCLUDED UNDER RESPIRATOR PROGRAM

JOB DESCRIPTION/             TYPE

NAME       DEPARTMENT    WORK PROCEDURE     RESPIRATOR

________   ______________     ___________________   _____________

________   ______________     ___________________   _____________

________   ______________     ___________________   _____________

________   ______________     ___________________   _____________

________   ______________     ___________________   _____________

- Emergency use procedures

The  following  work  areas  or  departments   have  been  identified  as

having  foreseeable  emergencies. Respirators may be for responding to

emergencies or for escape only.

DEPARTMENT/    FORSEEABLE         TYPE             RESPIRATOR

WORK AREA       EMERGENCY     RESPIRATOR      LOCATION

_____________     _____________    ____________      ___________

_____________     _____________    ____________      ___________

_____________     _____________    ____________      ___________

_____________     _____________    ____________      ___________

_____________     _____________    ____________      ___________

- IDLH (Immediately dangerous to life and health) procedures

a. One  or  more trained  and  equipped  standby person  stays outside

the IDLH atmosphere.

b. Visual, voice or signal  line communication  is maintained with the

employee in the IDLH atmosphere.

c. The employer is notified before the standby person enters the IDLH

atmosphere to provide emergency rescue.

d. The employer must provide  assistance  appropriate to the situation.

e. Employees engaged in interior structural  fire fighting  use  SCBAs.

f.. Only Grade D breathing air must be used in  cylinders for supplied

air respirators

# _______________ (program administrator) has identified these areas  as

having the potential for IDLH conditions:

WORK                IDLH                   RESPIRATOR            RESPIRATOR

AREA           CONDITION             REQUIRED                 LOCATION

______          ___________           _____________             __________

______          ___________           _____________             __________

______          ___________           _____________             __________

______          ___________           _____________             __________

- Cleaning, Maintenance, Change Schedules and Storage

  - Respirators  are to  be cleaned and  disinfected  at the  cleaning   station

located at ________________________________________________.

  - Respirators issued for exclusive use of one employee must  be  cleaned

and disinfected as often as necessary to be kept clean.

  - Respirators issued to more than one person  must  be  cleaned  and  dis-

infected before being worn by different individuals.

  - Respirators  maintained  for  emergency  use must  be cleaned  and  dis-

infected after each use.

  - Respirators  used  in   fit  testing and training  must  be cleaned  and dis-

infected after each use.

  - Procedures for cleaning respirators.

    - Remove filters, cartridges, or canisters.  Disassemble  facepieces by   removing  diaphragms,  valve   assemblies,  hoses   or  other

components recommended  by  the manufacturer, removing  and

discarding or repairing defective parts.

    - Wash  components  in  warm  (43 C, 110 F) water  with  a  mild

detergent  or  with  a cleaner recommended by the manufacturer.

A stiff-bristled brush may be used to remove dirt.

    - Rinse components in warm running water, then drain.

    - When  the  cleaner  used  does  not  contain  a disinfecting agent,

respirator  components  should  be  immersed  for 2  minutes  in

either a solution made by adding  1 milliliter  of laundry  bleach

to  one  liter  of  water,  an  aqueous solution of iodine  made by

adding approximately 0.8 milliliters of tincture of  iodine/100 cc

of  45 % alcohol  to 1 liter  of  warm  water, or  another cleanser

of equivalent  disinfectant quality  when  used  as recommended

or approved by the manufacturer.

    - Components  should  be  hand-dried with  a  clean lint-free cloth

or  air dried.

    - Reassemble facepiece, replacing filters,  cartridges  and  canisters

where necessary.

    - Test  the  respirator  to  ensure that all components work properly.

  - Respirators must be stored in a clean, dry  place,  so as  not to deform the

facepiece.

    - Respirators for general use will be stored  in________________

(location or locations).

    - Emergency use respirators will be stored in  cabinets  marked  as

emergency respirators at _____________________(locations).

  - Maintenance of respirators.

    - Respirators  for  routine  use  must  be inspected before each use

during cleaning.

    - Emergency  use  respirators  must  be inspected at least monthly

and as recommended by the manufacturer.

    - Emergency  escape-only  respirators  must  be  inspected before

being placed in service.

    - Respirator inspections must include at least the following:

      - A check of respirator function, tightness of connections, and  the  condition  of the facepiece, head straps, valves,

connecting  tubes,  and  cartridges ,   canisters  or  filters.

      - A check of elastomeric parts  for  pliability and  signs of

deterioration.

      - SCBAs  must  be  inspected  monthly .  Air  and Oxygen

cylinders  must  be  kept  in  fully  charged  state  and  be

recharged   when   the  pressure   falls   to   below   90 %.

Regulator  and   warning  devices  must  be  checked  for

proper working condition.

      - For emergency use respirators, a certificate documenting

the  date,  signature of  inspector,  the  required  remedial

action  and    serial  number  of  the  respirator   must   be

maintained.

  - Repairs

      - Repairs are to be made only by ____________________

(name of  trained employee or vendor)  and   only   parts

from   the   respirator   manufacturer  that   are    NIOSH

approved shall be used.

      - Repairs must  be  made  according to the manufacturer’s

recommendations.

      - Reducing  and  admission valves, regulators, and  alarms

must  not  be  repaired  except  by the manufacturer or  a

technician trained by the manufacturer.

  - Change Schedule

      - Change schedules should be determined by the program administrator based on exposure levels and time of exposure or the use of an ESLI. (attach supporting documentation for change schedule).

- Breathing Air Quality and Use

  - Compressed and liquid oxygen must meet United States Pharmacopoeia

requirements for medical or breathing oxygen.

  - Compressed  breathing  air  must  meet   at  least   the  requirements  for

grade D breathing air, oxygen content 19.5-23.5%, Hydrocarbon content

of  5 mg/m3,   Carbon Monoxide  content  of  10  ppm  or  less, and lack

of noticeable odor.

  - Compressed    oxygen   must   not    be  used   in   atmosphere-supplying

respirators that have previously used compressed air.

  - Oxygen concentrations greater than 23.5% must  not  be  used  in  equip-

ment unless it was designed for oxygen service or distribution.

  - Cylinders used to supply breathing air to respirators must be tested  and

maintained  according  to  Department of Transportation  regulations  in

49 CFR parts 173 and 178,  and  be  accompanied  by a certificate  from

the supplier that the breathing air  meets the  requirements  for  Grade D

breathing  air,  and  that  the  moisture  content in  the cylinder  does not

exceed a dew point of –50 degrees F at 1 atmosphere  pressure.

f.   Compressors  used  to  supply  breathing air  must  be constructed and

situated so as to prevent entry of contaminated air,  minimize moisture

content so that the dew point at 1 atmosphere pressure is  10 degrees F

below the ambient temperature.

- Compressors must have in-line air-purifying sorbent beds and filters to

further  ensure  breathing  air  quality,  they  must  be  maintained  and

replaced periodically  following  the  manufacturer’s  instructions, and

tagged  with  the  most  recent  change  date  and  signature  of  person

changing them.

- Oil-lubricated  compressors  must  have  a  high temperature or carbon

monoxide alarm, or both, to monitor carbon  monoxide  levels.  If only

high  temperature  alarm  is  used,  the  air  supply must  be  monitored

before use, then twice weekly, to keep carbon monoxide  levels  below

10 ppm.

- Non-oil  lubricated   compressors  must not  produce carbon monoxide

levels  greater than 10%.

- Breathing  air  couplings  must be  incompatible  with  outlets for non-

respirable  worksite    air   or   other   gas   systems.   No  asphyxiating

substances are to be  allowed into the breathing air lines.

- Training and Information:  Effective respirator training must be provided

for employees required to wear respirators. The training must be compre-

hensive,  understandable,  and  must  be  provided   before   requiring  an

employee to use a respirator and  at least annually thereafter.

- Employees who are allowed to  voluntarily  wear dust masks must be

provided the basic information on respirators in Appendix D.

- Employees must be able to demonstrate at least :

  - why the respirator is necessary and how improper fit, usage, or

maintenance  can  compromise  the protection of the respirator;

b.   what  the  limitations   and  capabilities  of   the  respirator  are;

- how  to  use  the  respirator effectively in emergency situations,

including   situations   in   which  the   respirator   malfunctions.

- how  to  inspect,  put  on  and  remove, use,  and check the seal;

- what  the  procedures  are  for  maintenance  and  storage of the

respirator;

- how  to  recognize  medical signs and symptoms that may limit

or prevent the effective use of the respirator.

g.   the  general   requirements   of  the  OSHA  respirator standard.

- Retraining must be given when:

  - changes in the workplace or  the type of respirator  used occur;

  - it  becomes  obvious  by  employees’  knowledge  or use of the

respirator  that  the  employee  has  not  retained the  necessary

understanding or skill.

  - other  situations  arise  in  which  retraining  appears necessary.

- Program Evaluation

  - ____________________ (program administrator) is responsible  for

ensuring  that  the  written  respiratory  protection  program  is being

followed  and  for  consulting  employees to see if they are using the

respirators properly.

  - ____________________ (program administrator)  is responsible  for

assessing the effectiveness of the respiratory  protection  program by:

    - consulting employees required  to use  respirators  to identify

any problems and corrective measures necessary.

    - determining  if  appropriate  respirator  selection  is made for

the hazards to which the employee is exposed.

    - determining if respirator fit  allows the use  of  the  respirator

without interfering with  effective  workplace  performance.

iv.    determining if respirators are being maintained properly.

- Recordkeeping

  - A written  copy  of  this  program and  the  OSHA standard is kept in

___________________________ (location on site).

  - ________________________ (program administrator)  keeps copies

of medical evaluations.

  - ________________________ (program administrator) has copies of

fit  test   results  that  show  the  employees’  names,  type  of fit  test

performed, specific make, model, style, and size  of respirator tested,

date of  test,  the pass/fail  results  for  qualitative  fit  tests  or  the fit

factor  and  strip  chart  recording  or  other  recording  of  the fit test

results for quantitative fit tests.